## Slide 1: South African Identity Federation
Draft Technical Roadmap
July 2016

## Slide 2: Status quo as at July 2016 – SCA mesh federation
Mesh federation; no hub; no consent; no metadata signing
Cannot join eduGAIN without developing metadata practice statement and signing metadata

## Slide 3: Phase 1 – initial deployment
All stored data here (eases restore after disaster)
Separate servers for hub & metadata improves security; facilitates growth
This is the only bit end users generally see – and then maybe not (proxy endpoints)
Policy and practice statement development must happen in parallel

## Slide 4: Phase 1 – initial deployment
Pros
Fully functional hub & spoke federation
Assuming admin requirements, can join eduGAIN
Complete separation of hub & metadata handling functionality
All data / logs stored centrally
Cons
No redundancy
No resiliency (ESXi)
Geographically all in Cape Town
Crypto keys on disk

## Slide 5: Phase 1.5 – hardware resiliency
Deploy VMware vSphere enterprise, with vSAN + HA
  Or an equivalent platform
Gets us protection from hardware failure, and ability to do maintenance on VM layer without impacting service
No real dependencies on SAFIRE– can happen at any point during deployment.

## Slide 6: Phase 2 – introduce redundancy
Use BGP to announce the same address space from CPT and JNB, using AS prepends to prefer CPT
Use haproxy to load balance between active nodes, setting a cookie to ensure session integrity
Failure of this element means loss of syslog and consent database. Users must (re-)consent for every login – irritating, but not service affecting
Because of caching, loss of metadata is non-service-affecting for about a day

## Slide 7: Phase 2 – introduce redundancy
Pros
Redundant hub and BIRK proxy endpoints – these are the bits people will notice if broken
Geographically dispersed
High availability through failover
Scalable architecture – add more nodes if we need to
Cons
No redundancy for metadata or web – but are these necessary?
  Not unless load is a problem.
No redundancy for DB, but understood failure mode
  Replication of the database might affect performance.
Crypto keys still on disk

## Slide 8: Phase 3 – introduce HSM
Initially perhaps something akin to a Raspberry Pi + smartcard based HSM. Fast enough for metadata signing, but not SAML

## Slide 9: Phase 3 – introduce HSM
Pros
Metadata signing key protected – this is the crucial key, because is the hardest to roll over
Cons
Will need to perform key rollover for metadata key
Smartcard based HSMs come with failure/backup concerns
  Have multiple offline cards
SAML assertion signing key still on disk
  Can be rolled over in metadata within 24 hours
Web server key still on disk
  Can be revoked by CA
Single point for failure for logging, no escrow
This is what the rest of the world expects of a “production” federation.

## Slide 10: Elements that are missing from the roadmap
Self-service metadata management
Monitoring
Statistics
Log escrow (remote syslog)
Hardware Security Module + operational practices